## Slide 1
ECEN 361
Real-Time and Embedded Systems
IOT - Information - Sampling
Notes: &&& Need to add more to this lecture – not enough meat

## Slide 2
Wave in Distance

## Slide 3
height
Wave in Time
time

## Slide 4
Storing Information in the Computer
height
time
Can we store this in the computer?

## Slide 5
Storing Information in the Computer
height
time
What if I want to analyze the information?

## Slide 6
Storing Information in the Computer
height
time
wave[] = 0, 3, 5, 7, 8, 9, 8, 7, 5, 3, 0, …

## Slide 7: Sampling x(t)
What is sampling?
Sampling Process
    Convert x(t) to numbers x[n]
    “n” is an integer; x[n] is a sequence of values
    Think of “n” as the storage address in memory
Uniform Sampling at t = nTs
    ideal: x[n] = x(nTs)
A-to-D
x(t)
x[n]

## Slide 8: Sampling Rate, fs
Sampling Rate (fs)?
  fs =1/Ts
    Number of Samples per Second
  Ts = 125 microsec  fs =
      Units are Hertz: 8000 Hz
Uniform Sampling at t = nTs = n/fs
  ideal: x[n] = x(nTs)=x(n/fs)
A-to-D
x(t)
x[n]=x(nTs)
8000 samples/sec

## Slide 9: Sampling Example

## Slide 10: Sampling Example

## Slide 11: Sampling Example

## Slide 12: Sampling Example
x[n] = {0.4, 0.8, 1.2, 1.5, 1.96} ?
What does the data look like?
x[n] = {204, 408, 612, 1536, 2007}

## Slide 13: Sampling Example
What does time look like?
0.1 seconds

## Slide 14
Sampling Example
How many samples/period do we get?
fs/f = samp/period
20 samp/period
5 samp/period

## Slide 15: Digital Frequency
varies from 0 to 2p, as f varies from 0 to the sampling frequency
Units are radians, not rad/sec
  Digital Frequency is Normalized

## Slide 16: Sampling Theorem
So, how often should we sample?
  Depends on the frequency of the signal
  Answered by Shannon/Nyquist Theorem
  Also depends on reconstruction needs

## Slide 17: Digital Sound
x(t) is a Black Eye Pea song (or Mormon Tabernacle Choir )
  How fast should we sample it?
Audio CD
  CD rate is 44,100 samples per second
  16-bits/sample
  Stereo - uses 2 channels
Number of bytes for 1 minute of the song?
  2 * (16/8) * 60 * 44100 = 10.584 Mbytes
What happens if we don’t sample at ≥ 2fmax?

## Slide 18: Spectrum of a Digital Signal
2p(0.1)
–0.2p
What does this mean?

## Slide 19: Another Digital Spectrum What does this mean?
2p(1)
–2p
?
x[n] is zero frequency???

## Slide 20: Reconstruction?
Given the samples, draw a sinusoid through the values

## Slide 21: Periodic Spectrum
Spectrum of x[n] has more than one line for each sinusoid
  Called Aliasing
Spectrum is periodic with period = 2p
  Because

## Slide 22: Aliasing Derivation
Other Frequencies give the same

## Slide 23: Aliasing Summary
Adding fs or 2fs or –fs to the Freq of x(t) gives exactly the same x[n]
  The samples, x[n] = x(n/ fs ) are exactly the same value
Given x[n], we can’t distinguish fo from (fo + fs ) or (fo + 2fs )
Normalized Radian Frequency