## Slide 1: ECEN 390 Electromagnetics
Transmission Lines 2

## Slide 2: Impedance Matching
.
Consequently,
need = R + j0 for typical impedance matching network.
With the matching network approach, reflections are eliminated
from the feedline, i.e., from the generator terminals to MM’, but not
necessarily from the load to the input of the matching network,
i.e., from AA’ to MM’ in the adjacent figures.
Smith Chart aids in impedance matching network calculations.

## Slide 3: Voltage Reflection Coefficients Plane
Smith Chart is a graphical way to design impedance-matching circuits
for ac steady-state.
Constant values are circles around the origin on Smith Charts.
Magnitude of the reflection coefficient, i.e.,
Point A in polar plot:
Notice that points C and D have inverse values, with = 0 for point C and = ∞ for point D. Impedance associated with point D equals 1/ of the impedance associated with point C.

## Slide 4: Smith Charts (Continued)
multiply both numerator and denominator
by the complex conjugate of the denominator.
These equations imply that many different and combinations result for any given or value.
Locus of (, ) points for a given (red) in the Complex Reflection Coefficient Plane.
Locus of (, ) points for a given (blue) in the Complex Reflection Coefficient Plane.

## Slide 5: Smith Charts (Continued)

## Slide 6: Smith Charts (Continued)
Since at the center = 0, the center of all rL (red) circles is on the real axis.
For rL = 0, the center is located at
For rL = 0.5, the center is located at
For rL = 1, the center is located at
For rL = 1.5, the center is located at
For rL = 2, the center is located at
For rL = ∞, the center is located at
The center of each rL circle is along the (real) axis and shifts to the right with shrinking radius as rL increases.

## Slide 7: Smith Charts (Continued)

## Slide 8: Smith Charts (Continued)
For xL = 0, the center is located at
For xL = 0.5, the center is located at
For xL = 1, the center is located at
For xL = 1.5, the center is located at
For xL = 2, the center is located at
For xL = ∞, the center is located at
The center of each xL circle is located on the vertical line with decreasing radius for increasing magnitude xL.

## Slide 9: Smith Charts (Continued)
There are four values for each point on a Smith chart, two values corresponding to the complex reflection coefficient and two values corresponding to the normalized impedance jx.
Constant values result in circles around the origin () on Smith Charts. Also, since
a given circle corresponds to a given VSWR circle, referred to as SWR circle on Smith Charts.
A complete 360˚ traversal of a SWR circle corresponds to
traversing a distance along a transmission line of λ/2.
Therefore, a 180˚ traversal around a SWR circle corresponds
to traversing a distance along a transmission line of λ/4.
Rotating clockwise along a SWR circle is referred to as moving
Wavelength Towards Generator (WTG). Rotating counter-clockwise
along a SWR circle is referred to as moving Wavelength Towards
Load (WTL).
Both WTG and WTL scales are distance scales in terms of λ,
used to determine required transmission line lengths for
impedance matching.
SWR Circle

## Slide 10: Smith Chart – WTG and WTL Outer Circles
Wavelength Toward Generator(WTG) in terms of λ.
Wavelength Toward Load (WTL) in terms of λ.
0λ

## Slide 11: Interactive Smith Chart
Go to Applied Electromagnetics 8E Textbook Website to run the Interactive Modules, located under Student Resources. Choose module 2.6 – Interactive Smith Chart for this activity.
The Interactive Smith Chart provides Impedance and Admittance information, along with distances along the transmission line in terms of λ.
Notes: Go to web Fundamentals of Applied Electromagnetics to download Interactive Modules available for the Ulaby – Fundamentals of Applied Electromagnetics text. Windows 10 has Java security issues that can be fixed as follows:
Java → Java Security → See Security Tab → Exception Site List. Add the following to the Exception Site List: http://em7e.eecs.umich.edu.

## Slide 12: Smith Chart Example 1
Using a Smith Chart, determine Zin for the adjacent circuit, given ZL = 60 + j40.
.
39.8 - j32.0
d = 0.2λ towards Generator.
Distance d Course Slider Adjust.
Distance d Fine Slider Adjust.
WTG Slider Adjustment.
WTG
ZL
Zin
Left/Right Arrow Keys can also be used.

## Slide 13: Smith Chart Example 2
Using a Smith Chart, determine ZL for the adjacent circuit, given Zin = 39.8 - j32.0 .
.
60 + j40
d = 0.5λ - 0.2λ = 0.3λ WTG.
Distance d Course Adjust Slider.
Distance d Fine Adjust Slider.
WTG Slider Adjustment.
Since slider only goes WTG, move slider to 0.5λ - 0.2λ = 0.3λ WTG to achieve 0.2λ WTL.
0.2λ WTL
0.3λ WTG
Poll Questions
Left/Right Arrow Keys can also be used.

## Slide 14: Smith Chart – Angle of Reflection Coefficient
Angle of Reflection Coefficient in Degrees
Angle of Transmission Coefficient in Degrees
±180˚
0˚
Voltage Transmission Coefficient is the ratio of the transmitted to incident voltage at an impedance discontinuity, given as T = 1 + .

## Slide 15: Smith Chart – Origin and Real Γr Axis
Real Reflection coefficient Axis on a Smith Chart is marked with normalized r values with r = 1 at the origin, i.e., . r < 1 to the left of the origin and r > 1 to the right of the origin.
Origin on the Smith Chart:

## Slide 16: Smith Chart – Horizontal Scales
Mark the distance from the origin ( 0 + j0) to a Reflection Coefficient Point and then determine the magnitude from the Reflection Coeffient Magnitude E or I scale shown above.
Reflection Coefficient Magnitude E or I
CENTER (0 distance reference) for Reflection Coefficient Magnitude ranging from 0 to 1.
Increasing Reflection Coefficient Magnitude

## Slide 17: Smith Charts (Continued)
Point | = | 
A |  | 
B |  | 
C |  | 
D |  | 
Point |  | 
A |  | 
B |  | 
C |  | 
D |  | 
A
D
B
C
0 + j0 ↔ 0 1 + j0 (matched)
-1 + j0 ↔ 1 0 + j0 (short)
1 + j0 ↔ 1 ∞ + j0 (open)
0.52 – j0.64 ↔ 0.825 0.5 – j2 (capacitive)

## Slide 18: SWR Circles
The light blue circle with origin () in the
adjacent graph corresponds to a constant value, which
also corresponds to a circle of constant voltage standing
Smith Charts are based on the voltage reflection coefficient,
rather than the current reflection coefficient. Consequently,
the acronym SWR for Standing Wave Ratio on a Smith Chart
refers to Voltage Standing Wave Ratio.
Constant or SWR circles on a Smith Chart are referred
to as SWR circles because the point these circles intersect the
axis, such as Pmax in the adjacent diagram, equals the VSWR
value for a given transmission line and load.
Hence, circles with their origin at () that pass through an impedance point of interest are called SWR circles.

## Slide 19: Impedance and Admittance Transformations
Impedance:
Admittance Y = 1/Z is easier to work with for parallel complex elements.

## Slide 20
Determine the equivalent admittance of the adjacent circuit,
at a frequency of 10 kHz.
Admittance Example

## Slide 21: Impedance and Admittance (Continued)
Rotation by λ/4 (180˚) on the SWR circle of a Smith Chart converts from z to 1/z = y and vice versa.

## Slide 22: Impedance and Admittance (Continued)
Rotation by λ/4 (180˚) on the SWR circle of a Smith Chart converts from z to 1/z = y and vice versa.
Smith Chart can be used either as an impedance
or admittance chart.
When used as an admittance chart, the
circles become circles.
Admittance is more convenient for parallel
(shunt) circuits.
In the adjacent Smith Chart normalized
impedance at point A represents
0.6 + j1.4  1.5232 =0.66).
Translating to point B by λ/4 on the
constant SWR circle results in a
normalized load admittance of
0.25 – j0.6  0.65) ≈ 1/.
Can also arrive at B by drawing straight line from A through origin and intersect constant SWR circle.
Poll Questions

## Slide 23: Back to Impedance Matching
Transmission line is said to be matched to the load when the characteristic impedance of a matching network, which prevents reflections along the feedline back to the source. So want Zin at MM’ to equal of the feedline.
Smith Chart aids in impedance matching network calculations.
Use a matching network to eliminate reflections at terminals MM’
for waves incident from the source.
So want Zin at MM’ to equal of the feedline. For a lossless
transmission line
of a lossless transmission line is a real number. Consequently, the matching network has to transform the real part of load impedance RL to R0 at MM’, and transform the reactive part of load impedance XL to zero at MM’.
Lumped-Element Matching involves adding a shunt (parallel) capacitor or inductor located at the appropriate distance from the load to achieve the desired Zin.
Single-Stub Matching involves adding a shorted transmission line, referred to as a stub, located at the appropriate distance from the load to achieve the desired Zin. Remember a shorted transmission line can produce inductive or capacitive reactance by choosing the appropriate line length relative to the wavelength of interest.

## Slide 24: Lumped Element Matching
Use a matching network to eliminate reflections at terminals MM’
for waves incident from the source.
Use admittance because of shunt (parallel) elements. In the admittance
domain, circles become circles and arcs become arcs.
So want Yin at MM’ to equal of the feedline. For a lossless
transmission line
, where is the input admittance of the line at MM’
from the load and is the admittance of the shunt element, either a
capacitor or an inductor, i.e., a reactive component.
. .
Using normalized quantities, normalized to .
For normalized admittance, want yin at MM’ to equal 1 + j0. Then scale by to get desired Yin value at MM’.
Consequently, want where bd is the normalized susceptance at distance d from the load.
corresponds to the circle on the Smith Chart and is achieved by proper shunt element placement.

## Slide 25: Lumped Element Matching Using Interactive Smith Chart
Smith Chart Solution procedure for Example 2-13: Determine both the distance in wavelengths from the load and value of a shunt element, i.e., inductor or capacitor, necessary to eliminate reflections from the load to the generator for a load impedance of connected to a 50 Ω transmission line at f = 100 MHz.
circle (grey) passes through the origin ().
Normalized .
Normalized .
SWR circle (magenta)
Update the new ZL and check
the y(d) box in upper right.

## Slide 26: Lumped Element Matching (Continued)
Smith Chart Solution procedure for Example 2-13: Determine both the distance in wavelengths from the load and value of a shunt element, i.e., inductor or capacitor, necessary to eliminate reflections from the load to the generator for a load impedance of connected to a 50 Ω transmission line at f = 100 MHz.
Next adjust slider bar d at the top of the window,
or use Left/Right arrow keys, so that y(d) (blue dot)
is moved to intersect the circle at both
intersection points, the inductive point corresponding
to the top half of the Smith Chart (Point C), and the
capacitive point corresponding to the bottom half of
the Smith Chart (Point D). referred to as point D. Read
off the resulting d value in terms of λ at each point.
  Point C: .
  Point D: .
Note that the adjacent Smith Chart is adjusted for
point C, i.e., dC, and not point D for dD.
Either a shunt inductor located at distance or a shunt capacitor located at
Point C
Point D

## Slide 27: Lumped Element Matching Using Standard Smith Chart
Smith Chart Solution procedure for Example 2-13: Determine both the distance in wavelengths from the load and value of a shunt element, i.e., inductor or capacitor, necessary to eliminate reflections from the matching network to the generator for a load impedance of connected to a 50 Ω transmission line at f = 100 MHz.
Normalized load impedance (Point A).
Using blue constant SWR circle and straight edge, point B
represents normalized load admittance .
WTG value for Moving along a SWR circle on
a Smith chart corresponds to moving along the length of a
given transmission line.
Red circle represents circle, with two intersection
points with SWR circle, C and D, representing two possible
solutions:
  Point C: . .
    .
  Point D: .
    .
D

## Slide 28: Lumped Element Matching Example 2-13: (Continued)
(From previous slides) Either a shunt inductor located at distance or a shunt capacitor located at will match the impedance of the 50 Ω transmission line at f = 100 MHz with .
Solve for shunt admittance so that
=
Point C:
A shunt 50.3 nH inductor located at 0.063λ from the load towards
the generator will eliminate reflections between the matching
network and the generator by matching Zin = 1/Yin = 50 Ω.
D

## Slide 29: Lumped Element Matching Example 2-13: (Continued)
(From previous slides) Either a shunt inductor located at distance or a shunt capacitor located at will match the impedance of the 50 Ω transmission line at f = 100 MHz with .
Solve for shunt admittance so that
=
Point D:
A shunt 50.4 pf capacitor located at from the load towards
the generator will eliminate reflections between the matching
network and the generator by matching Zin = 1/Yin = 50 Ω.
D

## Slide 30: Lumped Element Matching Example 2-13: (Continued)
    For a 50 Ω transmission line, Y0 = 1/Y0 =0.02 S.
    Point C: (Check)
Adding a 50 nH shunt inductor at distance 0.063λ from the load towards the
generator along the feedline eliminates reflections from the matching network
to the generator by matching Zin = 1/Yin = 50 Ω.
    Point D: (Check)
Adding a 50 pF shunt capacitor at distance 0.207λ from the load towards the generator along the feedline eliminates reflections from the matching network to the generator by matching Zin = 1/Yin = 50 Ω.

## Slide 31: Lumped Element Matching Summary
Use a matching network at terminals MM’ so as to eliminate reflections on
the feedline, which are undesirable for the generator.
Want Zin at MM’ = Z0, to eliminate feedline reflections.
Therefore, want normalized
Start with normalized load impedance: .
Convert to normalized load admittance, by mean of Smith Chart.
from the intersection of SWR circle with gL = 1 circle,
which results in Also record distance d in terms of λ from associated WTG value.
where is the normalize susceptance of the shunt element.
Want so determine shunt element L or C value needed for normalized shunt element admitance ys = -j.
Locate the shunt C or L element at appropriate distance d from load based on fractional λ value from WTG scale.
This results in which means that Yin = YO= YO, and therefore Zin = Z0, eliminating reflections between the feedline and matching network at MM’.

## Slide 32: Transients on Transmission Lines
Transient response deals with initial transients on transmission lines, such as when a logic gate switches output states on a high-speed PCB.
Lossless Lumped Element Transmission Line model consists of two basic elements:
L’ - combined inductance of both conductors per unit length in H/m.
C’ – capacitance of the two conductors per unit length in F/m.

## Slide 33: Transients on Transmission Lines (Continued)
For transmission lines that are electrically long, the resulting transient response is far from the ideal expected for an electrically short transmission line, and can result in erroneous digital data.
For adjacent transmission line at t = 0+, generator circuit only sees
characteristic impedance of the transmission line Z0.
For an infinitely long transmission line, the voltage at the generator
terminals always equals .
For practical transmission lines, reflections occur when impedances
are not matched. Time for first reflection at z = l equals T = l/up where up is the phase velocity of the waveform.

## Slide 34: Transients on Transmission Lines (Continued)
Initial wave-front at generator end:
First reflection from the load:
First returning reflection from the generator end:
Second reflection from the load:
Second returning reflection from the generator end:

## Slide 35: Transients on Transmission Lines (Continued)
The multiple reflection process continues indefinitely, and
the ultimate value that V(z, t) reaches as t approaches +∞ is
the same at all locations on the transmission line.
  Steady-state line voltage
  Steady-state line current
What about reflections occurring between Rg and
the generator terminals for Rg ≠ Z0?
This distance is often electrically short, so usually
can be ignored.

## Slide 36: Bounce Diagrams
Graphical representation of multiple reflections.
x-axis corresponds to distance along transmission line.
y-axis corresponds to time, with T corresponding to the
one way travel time along the transmission line.
Use reflection coefficients at load and generator to
determine magnitude associated with zig-zag lines.
Can construct resulting voltage or current at a given
distance along the transmission line utilizing vertical lines
at the desired distance. Total voltage or current is the
algebraic sum of individual zig-zag lines intersecting the
associated vertical line.
The adjacent voltage versus time diagram is for a
distance of l/4 down the line from the generator , which
is why the voltage equals zero until time t = T/4.

## Slide 37: Transient Response Example
For the adjacent circuit with Vg = 10 V, Rg = 75 Ω and Z0 = 75 Ω,
determine the resulting transient response waveform at switch
closure time t = 0 for the voltage at the input to the transmission
line, i.e., z = 0. The time T = l/up where up is the phase velocity of
the waveform down the transmission line.
5 V
-5 V

## Slide 38: Transient Response Example (Continued)
For the adjacent circuit with Vg = 10 V, Rg = 75 Ω and Z0 = 75 Ω,
determine the resulting transient response waveform at switch
closure time t = 0 for the voltage at the input to the transmission
line, i.e., z = 0. The time T = l/up where up is the phase velocity of
the waveform down the transmission line.
Vertical distance lines from the
Bounce Diagram provide the necessary
information to plot the resulting waveforms
at any distance l.
Poll Questions
V(t) at distance z = l, i.e., Load.
V(t) at distance z = 0, i.e., Generator.

## Slide 39: Digital Logic Bounce Diagram

## Slide 40: Digital Logic Bounce Diagram Continued)

## Slide 41: Digital Logic Bounce Diagram Continued)
9.090 V
5.372 V
1.654 V
4.696 V
5.249 V
7.738 V
2.760 V
4.545 V
4.545 V
5.372 V
4.696 V
5.249 V
9.090 V
1.654 V
7.738 V
2.760 V
0.000 V
0.000 V
4.545 V + 4.545 V = 9.090 V.

## Slide 42: Digital Logic Bounce Diagram with Termination Resistor

## Slide 43: Transient Response Measurement
Use Function Generator with relatively low-frequency square wave output with 20 V pk-pk amplitude for fast rise-time edge.
Use coaxial cable with Z0 ≈ Rg.
Notes: Go to web Fundamentals of Applied Electromagnetics to download Interactive Modules available for the Ulaby – Fundamentals of Applied Electromagnetics text. Windows 10 has Java security issues that can be fixed as follows:
Java → Java Security → See Security Tab → Exception Site List. Add the following to the Exception Site List: http://em7e.eecs.umich.edu.

## Slide 44: Transient Response Measurement Example
Use Function Generator with relatively low-frequency square wave output
with 20 V pk-pk amplitude for fast rise-time edge.
L = 75 ft = 22.86 meters. = 232 nS.
Calculate the

## Slide 45: Time Domain Reflectometer (TDR) for Cable Testing
TDRs consists of fast (< 200 ps) step generator and
fast sampler to measure the resulting signal voltage.
Expensive to dig up and repair buried cable.
for µr = 1 which is
true for most cables.
Location of unwanted impedance mismatch
can be determined by means of a TDR.

## Slide 46: Soil Moisture Measurements Using Permittivity
Irrigation water becoming a more precious resource.
Air has εr essentially equal to 1. Liquid H2O has εr = 80 @ 20 °C. Other soil constituents have εr < 10.
Therefore, is a strong function of water content of soil.
for µr = 1 which is true for soils.
in soils.
Permittivity sensors are commonly used to arrive at soil water content.
Standard equations available to convert from permittivity to soil water content.

## Slide 47: Time Domain Reflectometer (TDR) for Soil Moisture Measurements
TDRs consists of fast (< 200 ps) step generator and fast sampler to measure the resulting signal voltage.
Provides an excellent way to measure permittivity for soil water content.
TDR is preferred way to measure soil moisture content by research scientists.
TDR100 used for soil moisture measurements and costs ≈ $4000.
Less expensive TDR for soil moisture measurements is desirable and being pursued by multiple companies.
Open-Ended Transmission Line

## Slide 48: TDR for Soil Moisture Measurements (Continued)
Down and back travel time on TDR probe equals Δt = t2 – t1.
Standard equations convert to soil water content.
Voltage
Time
t1
t2

## Slide 49: Transmission Line Oscillator
Cost $200 per sensor.
Two rods inserted into the soil, forming an
open-ended transmission line.
Returning reflections trigger launching of
opposite polarity differential signal.
Oscillation frequency decreases for increasing water content, because .
Referred to as TDR (Time Domain Reflectometry) oscillator.
Some Soils have appreciable electrical conductivity which complicates measurements.

## Slide 50: ECEN 390 – Electromagnetics Topics
Waves and Phasors
Electrostatics
Transmission Lines
Vector Calculus
Magnetostatics
Time Varying Fields
Plane Wave Propagation
Radiation and Antennas
Satellites and Radar

## Slide 51: Extra

## Slide 52: Smith Charts (Continued)

## Slide 53: SWR, Voltage Maxima and Minima
As a result the circle corresponding to a
constant value also corresponds to a
circle of constant value and vice versa.
Points Pmax and Pmin correspond to
, where ,
Therefore,
where at intersection points
.

## Slide 54: Impedance Matching using Open Circuit Stubs

## Slide 55: SWR, Voltage Maxima and Minima (Continued)
Constant and therefore S corresponds to circles with center located at origin, i.e., = 0, = 0.
At Pmax, , which is the condition for
At Pmin, , which is the condition for
corresponds to point Pmax located on the axis (),
to the right of the chart center.
corresponds to point Pmin located on the axis (),
to the left of the chart center.
Pmax and Pmin represent locations of and,
and not power.
Total distance around the Smith chart is
Therefore, distance from to =

## Slide 56: Lumped Element Matching Example (Continued)
Solve for shunt admittance so that
  Point C:
  Point D:
D
D

## Slide 57: Smith Charts (Continued)
Point | = | 
A |  | 
B |  | 
C |  | 
D |  | 
Point |  | 
A |  | 
B |  | 
C |  | 
D |  | 
A
D
B
C
Given a value, how do you determine on a Smith Chart?
By using length ratios. Using a ruler, measure length , along with length determine as the ratio of This ratiometric measurement approach gives the correct ratio independent upon the size of the Smith Chart. Actual Smith Charts have a distance scale along the bottom to help with
How do you determine associated with on a Smith Chart?
Actual Smith Charts have a reflection coefficient angle scale (θr) along the perimeter
0 + j0 ↔ 0 1 + j0 (matched)
-1 + j0 ↔ 1 0 + j0 (short)
1 + j0 ↔ 1 ∞ + j0 (open)
0.52 – j0.64 ↔ 0.825 0.5 – j2 (capacitive)

## Slide 58: Transient Response Simulator
Go to web Fundamentals of Applied Electromagnetics to run or download Interactive Modules available for the Ulaby – “Fundamentals of Applied Electromagnetics” text. Run T-Line Simulator mod2-10_webstart.jnlp from Chapter 2 for this activity.
The Transient Response simulator provides transient response versus time waveforms for different line and load parameters. Transient Response mod2_10.
Notes: Go to web Fundamentals of Applied Electromagnetics to download Interactive Modules available for the Ulaby – Fundamentals of Applied Electromagnetics text. Windows 10 has Java security issues that can be fixed as follows:
Java → Java Security → See Security Tab → Exception Site List. Add the following to the Exception Site List: http://em7e.eecs.umich.edu.